## Slide 1
How we prepared Santiago data for Prof. Hohmeyer's RE100 model
We did not build a new model.
We used Prof. Hohmeyer's RE100 Excel model.
We replaced the Barbados data with Santiago, Cabo Verde data.

## Slide 2
What the model needs
Hourly load: how much electricity Santiago needs each hour.
Hourly wind speed: how much wind is available each hour.
Hourly solar radiation: how much sunlight is available each hour.
One normal year has 8760 hours.
Source: Prof. Hohmeyer RE100 Handbook, pages 15 and 16.

## Slide 3
The load data we already prepared
We used the DTU Santiago load profile.
DTU means Technical University of Denmark.
We scaled it to Electra's official 2023 Santiago annual production.
We checked the peak against Electra's 2023 Santiago peak.
Source: DTU dataset: https://data.dtu.dk/articles/dataset/Cape_Verde_Reference_System_v2_0/17430413. Electra report pages 25 and 26.

## Slide 4
Why we added wind data
The model needs wind speed for every hour.
We used Open-Meteo Historical Weather API.
We used Santiago coordinates.
We downloaded 2023 hourly wind speed at 100 m.
Because this is 100 m wind, the model input height must be 100 m.
Source: Open-Meteo docs: https://open-meteo.com/en/docs/historical-weather-api. Request: https://archive-api.open-meteo.com/v1/archive?latitude=14.9167&longitude=-23.5167&start_date=2023-01-01&end_date=2023-12-31&hourly=wind_speed_100m,shortwave_radiation&wind_speed_unit=ms&timezone=Atlantic%2FCape_Verde

## Slide 5
Why we added solar data
The model needs solar radiation for every hour.
Solar radiation means sunlight energy reaching the ground.
Open-Meteo gives it in W/m2.
The model needs kW/m2.
So we divided by 1000.
Source: Open-Meteo docs: https://open-meteo.com/en/docs/historical-weather-api. Request: https://archive-api.open-meteo.com/v1/archive?latitude=14.9167&longitude=-23.5167&start_date=2023-01-01&end_date=2023-12-31&hourly=wind_speed_100m,shortwave_radiation&wind_speed_unit=ms&timezone=Atlantic%2FCape_Verde

## Slide 6
Where the data goes in the model
Load goes into Hourly Load column F.
Wind goes into Wind and Solar Input column D.
Solar goes into Wind and Solar Input column E.
We kept the professor's formulas unchanged.
Source: Prof. Hohmeyer RE100 Handbook, pages 15 and 16.

## Slide 7
What is official and what is not
Official: Electra annual Santiago 2023 production.
Official: Electra Santiago 2023 peak.
Research source: DTU Santiago load profile.
Weather source: Open-Meteo hourly wind and solar.
Not official: exact 8760-hour SCADA load data, because it was not public.
SCADA means the operator's real control-room meter data.

## Slide 8
What we put in GitHub
raw data files
processed 8760-hour model input files
source links
method notes
presentation
professor workbook not uploaded unless permission is confirmed

## Slide 9
What we can defend
We can defend the annual load total.
We can defend the peak check.
We can defend where wind and solar came from.
We can defend how units were converted.
We cannot call reconstructed hourly load official meter data without Electra's real file.

## Slide 10
Final simple conclusion
We prepared the Santiago input data needed for the RE100 model.
The model can now use Santiago load, wind, and solar instead of Barbados data.
The work is documented so every value can be traced to a source.